## Slide 1
pH SENSOR
Principles, Types, and Real-World Applications
Presented by:
M. Sanjay Krishna(192525421)
Guided by:
Dr . M. Prakash

## Slide 2
What Is a pH Sensor?
A device that measures the hydrogen-ion (H⁺) activity in a solution, reporting acidity or alkalinity on the 0–14 pH scale.
1
Glass Membrane
A thin, pH-sensitive glass bulb separates the sample from an internal reference solution.
2
Ion Exchange
H⁺ ions interact with the membrane surface, creating a small voltage proportional to pH.
3
Voltage Reading
A reference electrode completes the circuit; the meter converts millivolts to a pH value.
4
Nernst Equation
Output follows ~59.16 mV per pH unit at 25°C, the theoretical Nernstian slope.
The pH Scale
0
7 (neutral)
14
Acidic
Basic
Probe Cross-Section
Reference electrode wire
Internal reference solution (KCl)
Ag/AgCl reference element
pH-sensitive glass membrane
Porous junction (electrical contact)

## Slide 3
Types of pH Sensors
1
Glass Electrode
Most common & accurate (±0.01 pH)
Fragile; needs regular calibration
Standard for labs & process control
2
ISFET (Solid-State)
Ion-Sensitive Field-Effect Transistor
Durable, shatterproof, fast response
Good for field & portable meters
3
Optical (Colorimetric)
Uses dye indicators & light absorbance
No electrodes to foul or drift
Suited to micro-volume samples

## Slide 4
Where pH Sensors Are Used
Water & Wastewater
Monitoring treatment plants, rivers, and drinking-water quality.
Food & Beverage
Controlling fermentation, dairy, and quality-assurance checks.
Agriculture
Testing soil and hydroponic nutrient-solution balance.
Medical & Pharma
Blood gas analysis, drug formulation, and diagnostics.
Chemical Manufacturing
Reaction control and neutralization in process lines.
Environmental Monitoring
Tracking ocean acidification and ecosystem health.

## Slide 5
System Architecture
pH Probe
Glass electrode +
reference
Signal
Conditioning
Preamp &
impedance buffer
ADC
Analog-to-digital
conversion
Microcontroller
Linearization &
calibration
Display / Output
Reading, alarms,
logging
Temperature Sensor
Auto-compensation (ATC)
Power Supply
Battery / mains regulation
Calibration Buffers
2-3 point calibration input
Communication
I²C / UART / Bluetooth → cloud or PLC

## Slide 6
Advantages & Limitations
+
Advantages
Fast, accurate, real-time readings
Wide measurement range (0–14 pH)
Available in portable & inline formats
Enables automated process control
−
Limitations
Glass electrodes are fragile & drift over time
Requires periodic calibration with buffers
Temperature affects readings (needs compensation)
Electrodes can foul in dirty samples